## Slide 1
Energy Efficient Scheduling in Data Centers
Debdeep Paul*, Wen-De Zhong*,
Sanjay K. Bose**
* School of Electrical and Electronic Engineering, NTU Singapore
** Dept. of EEE, IITG, India

## Slide 2: Outline
Motivation and background
Model
Two scheduling procedures
Results
Conclusions

## Slide 3: Motivation
Data centers are energy hogs
Energy consumed by data centers 2-3% of the total energy consumed in the US
And it is growing 12~15% a year, US electricity growth 1%

## Slide 4: Background
Energy efficiency in data centers, enormous improvements in last few decades
  Building energy management: cooling, lighting
  Dynamic right sizing: to turn off extra servers
  Geographical load balancing: follow the renewables
Recent focus on sustainability- e.g., renewable integration
Data centers are a promising option
  Unharnessed opportunities
    have significant flexibility (building energy management, workload management- leveraging Slack e.g.,)
    highly automated

## Slide 5: Model: key ideas
Energy aware scheduling (Demand Response)
Different attributes through costs
Two optimization procedure:
  Electricity expense
  Server switching- from OFF to ON and vice versa
  Max servers
Capture the tiered
architecture of the data center
Deferrable and non deferrable jobs (Scientific simulations.., Real time..)

## Slide 6: Scheduling procedure-I: CapexOpexMin Key ideas
Power consumed
Power cost; co-located renewables
 Switching cost
 Peak server provisioning cost
 Safety margin
Constraints:
All jobs are serviced
QoS guarantee
Mapping from job request to # of servers to be provisioned
Total jobs= Deferrable + non deferrable jobs

## Slide 7: Scheduling procedure-I: CapexOpexMin
Convex problem– computationally tractable
Ensuring:
Individual deferrable jobs:
  Upper and lower bound on # of servers
Sum across all active jobs to obtain upper and lower bound on total # servers
Deferrable jobs are serviced before deadline
Total # of servers in each tier does not exceed # of servers present at that tier

## Slide 8: Scheduling procedure-II: OpexMin
s.t. same conditions as CapexOpexMin
Implement the algorithms in CVX, Matlab 7.11.0
CapexOpexMin- 3 sec and OpexMin- 2 sec to converge
Objective is to have effect of all the attributes in the overall objective function

## Slide 9: Simulation setup
Electricity price traces obtained from wholesale electricity market in Singapore
Real renewable energy trace
Job traces obtained from a commercial server cluster owned by Facebook
Assumed a data center with total 120K servers
Compared the proposed algorithms with the corresponding oracle counterpart with perfect future forecast

## Slide 10: Simulation results (1/4)
~ 14% peak reduction
Notes: Mention cumulative Electricity expenses

## Slide 11: Simulation results (2/4)
~ 21% reduction in electricity expense
Notes: Mention cumulative Electricity expenses

## Slide 12: Simulation results (3/4)
~ 70% reduction in # of switchings
Notes: Mention cumulative Electricity expenses

## Slide 13
 | CEC | CRC | CNS
CapexOpexMin over OpexMin | 21% | -12% | 70%
OpexMin Oracle over MPC | 34% | 2.17% | 93.3%
CapexOpexMin Oracle over MPC | -3% | 12.7% | 56.3%
Very sensitive to uncertainty
13.8% peak reduction, translates into $170~$340M
Simulation results (4/4)

## Slide 14: Conclusions
The proposed method achieves substantial server provisioning (capital) cost reduction
Capturing switching cost through variance imposes a better control, especially if frequent server switching is a concern
Capturing switching cost through variance reduces sensitivity with respect to optimization horizon, especially in terms of switching

## Slide 15: Previous works
[1] B. Urgaonkar, G. Pacifici, P. Shenoy, M. Spreitzer, and A. Tantawi, "An analytical model for multi-tier internet services and its applications," ACM SIGMETRICS 2005.
[2] A. Subramanian, M. J. Garcia, D. S. Callaway, K. Poolla, and P. Varaiya, "Real-time scheduling of distributed resources," IEEE Trans.Smart Grid, 2013.
[3] A. Krioukov, C. Goebel, S. Alspaugh, Y. Chen, D. E. Culler, and R. H. Katz, "Integrating renewable energy using data analytics systems: challenges and opportunities," IEEE Data Eng. Bull., 2011.

## Slide 16
Further queries:
debdeep1@e.ntu.edu.sg
Thank you so much!